## Slide 1: Thermal-Aware Power Budgeting for a Quad-Core RISC-V Processor
Using the heat equation and linear programming to keep the hottest point on the die as cool as possible
Notes: [about 15 s] Good morning. Our project is about deciding how to split a fixed power budget among the cores of a processor so the chip runs as cool as possible. I'll cover the problem, the maths we used, the software we built, and what the results show.

## Slide 2: Where should the 5 watts go?
1 INTRODUCTION
The problem
A 10 mm x 10 mm die holds four RISC-V cores and a shared L2 cache. The total budget is 5 W and the die edges sit at 300 K. Pick each block's power to minimize the peak temperature.
Why it matters
The hottest spot, not the average, sets when a chip throttles. Heat also raises leakage and wears out the silicon faster.
How we solved it
One chain of mathematics: heat PDE, Laplace transform, finite differences, then a linear program that uses the same matrix.
Core 0
Core 1
Core 2
Core 3
Shared L2
Edges held at 300 K by the heat sink. The L2 cache sits in the center, the worst-cooled spot.
Notes: [about 50 s] Picture a ten-millimetre die with four processor cores in the corners and a shared L2 cache in the middle. We have exactly five watts to hand out. The edges are bolted to a heat sink at 300 kelvin, so they stay cool, but the middle is far from the sink. What matters to a chip is its hottest point, because that is when firmware slows the clock down. So the question is: how do we split five watts to make the hottest point as low as possible? We treat it as one chain of maths rather than a simulation followed by guesswork.

## Slide 3: Our Embodiment: Why a Quad-Core RISC-V Chip
2 OUR EMBODIMENT
The Brief
Our Choice
Why RISC-V
Four heat-generating blocks sit on a 10 mm x 10 mm die that shares a 5 W budget. Choose each block's power to minimize the hottest point.
Core 0
Core 1
Core 2
Core 3
Shared L2
FRISC-V: published RV32I core, University of Zagreb, 2024
Open-source, FPGA-proven, and built for multicore
Rejected: Intel 8051, a microwatt, single-core design
Die size, grid, and budget match the brief exactly. We chose a specific architecture to make the thermal problem concrete.
Notes: [about 30 s] The brief describes a generic problem: four heat sources, five watts, a ten-millimetre die. To make it concrete we chose a real architecture, a quad-core RISC-V chip with a shared L2 cache in the centre. FRISC-V is a published open-source core, proven on an FPGA and able to boot Linux. We rejected the Intel 8051, whose microwatt budget is far too small for a five-watt problem.

## Slide 4: What exists, and what is left to do
3 RELATED WORK
Compact thermal models
Huang et al. [2]
Analytical conduction
Carslaw and Jaeger [1]
Convex optimization
Murali et al. [3]; Boyd and Vandenberghe [4]
The gap we address. Compact models lose the spatial field, and frequency-control methods do not put the full heat operator in the optimizer. Our pipeline keeps the whole 2D field and stays linear, so the optimizer and the physics share one matrix.
Notes: [about 15 s] Prior work falls into three groups: compact thermal models such as HotSpot, analytical conduction solutions from Carslaw and Jaeger, and convex optimization. Our gap is that the full spatial field and the optimizer share one matrix.

## Slide 5: From Fourier's law to a linear program
4 METHODOLOGY
1
Field model
Vector Calculus
q = -k∇T
∇·q = Q
Heat flows down the temperature gradient. Heat in equals heat out.
2
PDE
Elliptic
∇²T = -Q/k
A Poisson equation with T = 300 K on the edges. Every point feels every source.
3
Transform
Laplace in time
Zth(s) = ΔΘ(s) / P(s)
Each mode is a one-pole delay. As s → 0 it gives the steady thermal resistance.
4
Discretize
Linear Algebra
Aθ = Bq
Five-point stencil on a 40 x 40 grid gives a sparse 1600 x 1600 matrix.
5
Optimize
Linear Programming
min t
s.t. Aθ = Bq
θ ≤ t, Σq = 5 W
q ≥ 0, q(L2) ≥ 0.3 W
The variable t bounds every node, so minimizing t minimizes the peak.
Why this is an LP. Because θ = A⁻¹Bq is linear in the powers q, the peak is a maximum of linear functions. The extra variable t turns that maximum into ordinary linear constraints.
T: temperature (K) k: conductivity, 150 W/(m K) Q: heat generation s: Laplace variable Zth: thermal impedance (K/W) θ: temperature rise q: block powers (W) t: peak rise (K)
Notes: [about 70 s] Five steps, each from a different course. One: Fourier's law says heat flows down the temperature gradient, and an energy balance says what flows in equals what is generated. Two: together they give the Poisson equation, which is elliptic, with the die edges fixed at 300 kelvin. Three: taking the Laplace transform in time gives a thermal impedance Zth of s. Each spatial mode is a simple one-pole lag, and as s goes to zero it reduces to the steady thermal resistance, so solving only the steady problem is justified. Four: a five-point finite-difference stencil on a forty-by-forty grid gives A theta equals B q, a sparse sixteen-hundred-square matrix. Five: since theta is linear in the powers, the peak is a maximum of linear functions. Adding one variable t that bounds every node gives a linear program. The five watts are fixed, powers are non-negative, and the cache has a small minimum of 0.3 watts. That is why the optimization is a consequence of the physics and not a bolt-on.

## Slide 6: A modular Python pipeline
5 EXPERIMENTAL SETUP
The chip we model
The core design follows FRISC-V, a published open-source RV32I core with a 5-stage pipeline [6].
Four cores sit in the die quadrants and a shared L2 cache sits at the center, the usual layout that keeps wires short.
Blocks are flat rectangles on a 40 x 40 grid. The brief's four-point layout is kept as a validation case.
Tools
Python 3 with NumPy, SciPy (sparse matrices and linprog with the HiGHS solver [5]) and Matplotlib. A Tkinter dashboard reuses the same solver functions as the batch run.
1600 x 1600
sparse matrix A
16 / 16
unit tests pass
1 command
python run.py
Notes: [about 40 s] For the chip we chose a RISC-V quad-core, based on FRISC-V, an open-source five-stage RV32I core from the University of Zagreb. RISC-V suits multicore designs, it is open, and published power numbers exist, so a watt-level study is credible. We placed the four cores in the quadrants and the shared L2 cache at the centre, which is also the worst-cooled spot. Everything is Python: NumPy, SciPy sparse matrices, linprog with HiGHS, and Matplotlib. The code is one module per maths stage, the GUI reuses the same functions, sixteen automated tests pass, and one command rebuilds every figure.

## Slide 7: The LP lowers the peak by up to 5.79 K
6 RESULTS
Chart: Peak die temperature at 5 W (K)
| Scenario A: all cores active | Scenario B: cores 2 and 3 idle
Uniform split | 325.18 | 328.65
LP-optimal | 322.86 | 322.86
Case | Uniform (K) | LP (K) | Drop (K)
A: all cores active | 325.18 | 322.86 | 2.31
B: two cores idle | 328.65 | 322.86 | 5.79
Brief's 4-point layout | 343.45 | 343.45 | 0.00
Both scenarios end at the same plan: 1.175 W per core and 0.300 W for the L2 cache. The LP works on the physics, not the workload, so equal core power with a minimal cache wins. The idle cores in B simply made the uniform split worse.
5.79 K
lower peak when two cores idle
4.03 vs 5.73 K/W
peak rise per watt, LP vs uniform
5.91 x 10⁻¹⁶
modal vs sparse solver error
Notes: [about 70 s] Here are the numbers. With all four cores active, the uniform split peaks at 325.18 kelvin and the LP at 322.86, a 2.3 kelvin drop. When only two cores are busy, the uniform split gets worse, 328.65, but the LP lands on the same 322.86 K, a 5.79 kelvin reduction. The reason is that the LP works on the physics, not the workload: the cores are thermally symmetric and the cache is worst-cooled, so equal core power of 1.175 watts and the minimum 0.3 watts for the cache is best in both cases. The last row is our check on the brief's own four-point layout. Its blocks are mirror images, so uniform is already optimal and the gain is zero. Sweeping the budget from 1 to 8 watts, the peak rises 4.03 K per watt with the LP against 5.73 uniform, so the benefit grows with power. Finally, the analytical modal solution and the sparse solver agree to 6e-16, which is machine precision.

## Slide 8: What we can claim, and what we cannot
7 LIMITATIONS AND CONCLUSION
Synthetic power
Block powers come from a model, not from measured RISC-V silicon.
Simple die
Constant conductivity, ideal 300 K edges, and no package or heat spreader.
The cache floor matters
The 0.3 W minimum for L2 shapes the answer. A different floor moves the optimum.
Brief's target
With the brief's symmetric layout, uniform is already optimal, so the expected 5 K gain cannot appear.
Conclusion
The LP allocation cuts the peak by 5.79 K when two cores are idle and by 2.31 K when all four run.
Every stage is checked, with 16 of 16 tests passing and machine-precision agreement with the analytical solution.
Next steps: finite-area blocks with measured power, a 3D package model, and transient workloads.
Notes: [about 50 s] Some honest limits. The power numbers are modelled, not measured. The die is idealised: constant conductivity, perfect heat-sink edges, and no package. The 0.3 watt cache minimum influences the answer. And with the brief's perfectly symmetric four-point layout, uniform is already optimal, so the expected five kelvin gain cannot appear; we show that as a validation case rather than force a result. To conclude: the LP lowers the peak by 5.79 kelvin for the asymmetric workload, every stage is verified, and one command reproduces everything. Next we would use finite-area blocks with measured power, a 3D package model, and transient workloads.

## Slide 9: References
8 REFERENCES
[1] H. S. Carslaw and J. C. Jaeger, Conduction of Heat in Solids, 2nd ed., Oxford University Press, 1959.
[2] W. Huang et al., "HotSpot: A compact thermal modeling methodology for early-stage VLSI design," IEEE Trans. VLSI Syst., vol. 14, no. 5, 2006.
[3] S. Murali et al., "Temperature-aware processor frequency assignment for MPSoCs using convex optimization," CODES+ISSS, 2007.
[4] S. Boyd and L. Vandenberghe, Convex Optimization, Cambridge University Press, 2004.
[5] P. Virtanen et al., "SciPy 1.0: Fundamental algorithms for scientific computing in Python," Nature Methods, vol. 17, 2020.
[6] FRISC-V, open-source 5-stage RV32I core, University of Zagreb, 2024.
Notes: [about 10 s] These are the references. Thank you, we are happy to take questions. Total target time: about 6 minutes.